## Slide 1: SI Units & Ohms Law
Year 10 Electronics
Mr Wright

## Slide 2: Prefix Multipliers
1
0.001
0.000001
0.000000001
0.000000000001
1 milli (m)
10-3
1 micro (µ)
10-6
1 nano (n)
10-9
1 pico (p)
10-12
1,000
1 Kilo(K)
103
1,000,000
1 Mega (M)
106
1,000,000,000
1 Giga (G)
109
1,000,000,000,000
1 Tera (T)
1012

## Slide 3: SI Units
Voltage Volts
Current Amps
Resistance Ohms
Capacitance Farads
Time Seconds
Frequency Hertz
Power Watts
Charge Colombs
Energy Joules

## Slide 4: Ohms Law
V
I
R
V = IR
V = voltage (Volts)
I = current (Amps)
R = resistance (Ohms)
The most important equation you will ever learn in electronics

## Slide 5: Some Exercizes
What voltage must be applied to a 2kΩ resistor in order for a 10mA current to flow ?
A coil has a current of 50 mA flowing through it when the voltage is 12 V. What is the resistance of the coil?
A 100 V battery is connected across a resistor and causes a current of 5mA to flow. Determine the resistance of the resistor.
V
I
R

## Slide 6: What Else Does Ohm’s Law Tell us?
Rule 1:
  A resistor with a current flowing through it will always have a voltage drop across it
Example
X
+9V
0V
50mA
X
+9V
0V
50mA
R = 220Ω
The light bulb demands 50mA
In the left hand circuit it has 9V across it & its demand is met
If I insert a 220Ω resistor in series with the light bulb :
What current flows through the resistor ?
What current flows through the light bulb
3. what voltage does the light bulb see now

## Slide 7: Rule 1: Example 2
The LED will blow up if it sees more than 15mA
The LED has a voltage drop of 1.5V
The power supply is +5v
So what happens to the other 3.5V ?
What is the value of the resistor ?
V
I
R

## Slide 8: Rule 2:
A current cant exist without a voltage
I = V/R
If V = 0, then the value of R is irrelevant
  I will always = 0 (NOTHING DIVIDED BY SOMETHING IS ALWAYS NOTHING)
So if any part of your circuit cant see a voltage – it wont work !
V
I
R

## Slide 9: Rule 3:
The higher the resistance, the lower the current
  Resistors limit current
V
I
R

## Slide 10: Rule 4:
The lower the resistance the lower the voltage drop
V
I
R

## Slide 11: Potential Dividers
Potential Divider Simulator
The fact that resistors drop voltage across them can be used to create fractions of the supply voltage
Vs
0V
R1
R2
Vo

## Slide 12: Why Might I Want One ? (What use are they ?)
If I have 9v supply (for example):
  I might want 5v to drive part of my chip
  I might want just 1v to drive a transistor
I could use a second supply at a different voltage but deriving a lower voltage from the primary supply is more efficient

## Slide 13: Example 1
Resistors R1 & R2 are equal
Each will drop the same amount of voltage
The voltage seen at the output is exactly half the supply

## Slide 14: Example 2
R2 is 2x bigger than R1
R2 will drop 2x more voltage than R1
The voltage seen at the output is 2/3 of supply

## Slide 15: Its all about ratios !
If supply voltage = 9V and R1 =2k and R2 = 1k, R2 will drop half as much voltage as R1
The voltage seen at the output is 3v
If supply = 12V and R1 =2K and R2=1k, the output voltage will be ????
Vo = Vs R2 / (R1 + R2)

## Slide 16: Remember
The bigger the resistor, the bigger the voltage drop
Output voltage is always measured between 0V and the connection point of R1 & R2
What is difference between:
  A: supply = 9V, R1 = 1K, R2=2K
  B: supply = 9V, R1 = 100Ω, R2 = 200Ω

## Slide 17: Other ways of controlling voltage
The zener diode
This conducts only when the voltage accross it reaches a certain voltage

## Slide 18: DC Average Power
How much energy is transferred in a unit of time
  Burned or generated
Measured in Watts
Average power: P= IV
Things that affect how much power a circuit will use:
  Supply voltage
  Amount of time it is switched on for
  Activity (amount of switching)
P
I
V

## Slide 19: Why Is Power Important ?
Burning energy generates heat
If I have a resistor with 9V across it and 100mA flowing through it, I will burn 0.9 W
Resistors come in different power ratings
  Higher values are:
    Physically bigger
    Can dissipate more heat
    Cost a lot more
If your resistor cant handle the power of your circuit, it will melt & fail
Most resistors in school are 0.25W, 0.5W or 0.6W
  Metal film / carbon
Higher values (1W, 5W etc) are available
  Wire wound